## Slide 1: Week 7 Presentation
Team 16
By: James Panhorst, Jibin Mathews, Josh Ramirez, Alex Holmes

## Slide 2: Objectives
Develop an autonomous robot that can navigate racetrack and avoid obstacles
Must be able to:
  Follow Metallic Tape (IPS: LJ18A3-8-Z/BX)
  Avoid Obstacles (IR Sensor: GP2Y0A60SZ0F)
  Detect/ proceed actions with corresponding colors (Color Light-to-Frequency TCS3200)
    Green: Go
    Blue: Slow Down
    Red: Stop
Design Printed Circuit Boards (PCB) and utilize with project

## Slide 3: Approaches for objectives
IPS Sensor needs to be adjusted to the right height
  Corner Ramp
    Is the positioning of IPS affected?
    Is the ride height of the Rover 5 affected?
  Alternative Path
    How can the robot turn while still knowing to follow the metallic line using IPS?
      More proximity sensors(Maybe 4)
  Color Sensor
    Positioning (Underneath, Behind, In-front)

## Slide 4: Deliverables For Week 7
Finished the hardware for the IR sensor and successfully connected it to a comparator.
Implemented a 2nd IPS sensor and began connectivity tests to the Basys3.
Continued research on the color sensor.
Finished trial design of the base for the rover

## Slide 5: Gantt Chart

## Slide 6: Budget Sheet

## Slide 7: Rover 5 Base Model

## Slide 8: IR Sensor Details
Utilized an LM339 comparator to compare the IR sensor output to a fixed voltage.
The fixed voltage is a result of a voltage divider, resulting in 2.0V connected to the inverting terminal of the comparator.
The non-inverting terminal is connected to the IR sensor output.
A pull-up resistor is connected from the IR output to 3.3V supplied from the Basys3 board.
As a result, when the IR sensor outputs more than 2.0V when an object comes within 20cm of it, the comparator outputs a signal high.

## Slide 9: IR Sensor

## Slide 10: Inductive Proximity Sensor
Methods to implement proximity sensors to Basys3 Board?
-Voltage Divider
-Optocoupler

## Slide 11: TCS3200 frequency

## Slide 12: Pulse detection
https://www.chipverify.com/verilog/verilog-positive-edge-detector

## Slide 13: Next Week’s Deliverables
Finish testing and implementing code for the IR sensor.
Finish hooking up the IPS sensors to the Basys3.
Complete software implementations of the IPS sensors.
Make improvements/ changes to the trial base and print (3-D printer)
  Implement IPS and IR Sensor mounting to the base

## Slide 14: References
[1] IR Sensor (GP2Y0A60SZ0F) datasheet. https://www.pololu.com/file/0J812/gp2y0a60szxf_e.pdf.
[2] IPS Sensor (LJ18A3-8-Z/BX). http://files.microjpm.webnode.com/200003722-858c88684b/Condutive%20Proximity%20Switch%20Series.pdf
[3] Color Light-To-Frequency Converter (TCS3200) datasheet. https://www.mouser.com/catalog/specsheets/tcs3200-e11.pdf
[4] TCS3200 Tester Code. https://randomnerdtutorials.com/arduino-color-sensor-tcs230-tcs3200/

## Slide 15: Questions